## Slide 1
AL1x4x Setup PLC for reading process data
Configuring the AL1x4x IO-Link module
Setup PLC for reading process data

## Slide 2
1. Start CODESYS 3.5 SP12
2. Add Device
„Ethernet“ to
your project
AL1x4x Setup PLC for reading process data

## Slide 3
3. Add a Modbus TCP Master
4. Add a Modbus TCP Slave to the Modbus TCP master
AL1x4x Setup PLC for reading process data

## Slide 4
5. Type in the IP –Address of AL1x4x and Unit-ID [1]
AL1x4x Setup PLC for reading process data
6. Add Modbus Channels (Read Holding Registers)

## Slide 5
7. Define Variables for each IO-Link port and assign them in the mapping table of Modbus
AL1x4x Setup PLC for reading process data

## Slide 6
8. Add a function block ReadPD and shift the value for 4 Bits
(see IO-Link description PDF of the O5D150 )
AL1x4x Setup PLC for reading process data

## Slide 7
9. Start the CODESYS project on the AC14 PLC
AL1x4x Setup PLC for reading process data
10. Call the function block in your PLC_PRG, compile and download the project to your computer, start the application and type in the port number where the O5D150 is connected to